## Slide 1: Agenda
MIPS ISA
Sample Questions

## Slide 2: Review
Registers in MIPS
  Inside processor use for frequently accessed data and fast calculation
  How many registers in MIPS: 32
  How large are them: 32 bit
  How they work
    Load values from memory into registers
    Store result from register to memory

## Slide 3: Review
Registers in MIPS
  C code
  f = (g + h) – (i + j); // g, h, i, j in $s1-s4
  Compiled MIPS code
  add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 4: Review: Instructions in MIPS
3 simple formats
  R-type, 3 register operands
  I-type, 2 register operands and 16-bit immediate
  J-type, 26-bit immediate operand
Simple decoding
  4 bytes per instruction, regardless of format
  Must be 4-byte aligned
  Format and fields readily extractable

## Slide 5: ALU Instructions
Assembly (e.g. register-register signed addition)
  ADD rdreg rsreg rtreg
Machine encoding
Semantics
  GPR[rd] ← GPR[rs] + GPR[rt]
  PC ← PC + 4
Exception on overflow
Variations
  Arithmetic: {signed, unsigned} x {ADD, SUB}
  Logical: {AND, OR, XOR, NOR}
  Shift: {Left, Right-Logical, Right-Arithmetic}
0
6-bit
rs
5-bit
rt
5-bit
R-type
rd
5-bit
0
5-bit
ADD
6-bit

## Slide 6: ALU Instructions
Assembly (e.g. reg-immediate signed additions)
  ADDI rtreg rsreg immediate16
Machine encoding
Semantics
  GPR[rt] ← GPR[rs] + sign-extend (immediate)
  PC ← PC + 4
Exception on overflow
Variations
  Arithmetic: {signed, unsigned} x {ADD}
  Logical: {AND, OR, XOR, LUI}
ADDI
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type

## Slide 7: Load Instructions
Assembly (e.g. load 4-byte word)
  LW rtreg offset16 (basereg)
Machine encoding
Semantics
  effective_address = sign-extend(offset) + GPR[base]
  GPR[rt] ← MEM[ translate(effective_address) ]
  PC ← PC + 4
Exceptions
  Address must be word-aligned
  MMU exceptions
LW
6-bit
base
5-bit
rt
5-bit
offset
16-bit
I-type

## Slide 8: Store Instructions
Assembly (e.g. store 4-byte word)
  SW rtreg offset16 (basereg)
Machine encoding
Semantics
  effective_address = sign-extend(offset) + GPR[base]
  MEM[ translate(effective_address) ] ← GPR[rt]
  PC ← PC + 4
Exceptions
  Address must be word-aligned
  MMU exceptions
SW
6-bit
base
5-bit
rt
5-bit
offset
16-bit
I-type

## Slide 9: (Conditional) Branch Instructions
Assembly (e.g. branch if equal)
  BEQ rsreg rtreg immediate16
Machine encoding
Semantics
  immediate: relative word address
  branchAddr = sign-extend(immediate) x 4
  if GPR[rs]==GPR[rt] then PC ← PC + 4 + branchAddr else PC ← PC + 4
How far can you jump?
  Within -2^15 to 2^15 words of the current instruction
Variations
  BEQ, BNE, BLEZ, BGTZ
BEQ
6-bit
rs
5-bit
rt
5-bit
immediate
16-bit
I-type

## Slide 10: Jump Instructions
Assembly
  J immediate26
Machine encoding
Semantics
  immediate: word address
  jumpAddr = { PC + 4[31:28], immediate, 2’b0 }
  PC ← jumpAddr
How far can you jump?
  2^26 words not related to the current instruction
Variations
  Jump and link
  Jump registers
J
6-bit
immediate
26-bit
J-type

## Slide 11: ISA-level Tradeoffs: Instruction Length
Fixed length: Length of all instructions the same
  + Easier to decode single instruction in hardware
  + Easier to decode multiple instructions concurrently
  -- Wasted bits in instructions (Why is this bad?)
  -- Harder-to-extend ISA (how to add new instructions?)
Variable length: Length of instructions different
  + Compact encoding (Why is this good?)
  -- More logic to decode a single instruction
  -- Harder to decode multiple instructions concurrently
Tradeoffs
  Code size (memory space, bandwidth, latency) vs. hardware complexity
  ISA extensibility and expressiveness vs. hardware complexity
  Performance? Energy? Smaller code vs. ease of decode

## Slide 12: ISA-level Tradeoffs: Uniform Decode
Uniform decode: Same bits in each instruction correspond to the same meaning
  + Easier decode, simpler hardware
  + Enables parallelism: generate target address before knowing the instruction is a branch
  -- Restricts instruction format or wastes space
  e.g. MIPS, SPARC, Alpha
Non-uniform decode
  + More compact and powerful instruction format
  -- More complex decode logic
  e.g. opcode can be the 1st – 7th byte in x86

## Slide 13: ISA-level Tradeoffs: Number of Registers
Affects
  Number of bits used for encoding register address
  Number of values kept in fast storage (register file)
  Size, access time, power consumption of register file
Large number of registers:
  + enables better register allocation (and optimization) by compiler -> fewer saves/restores
  -- larger instruction size
  -- larger register file size

## Slide 14: ISA-level Tradeoffs: Addressing Modes
Addressing mode specifies how to obtain an operand of an instruction
  Register
  Immediate
  Memory (displacement, register indirect, indexed, absolute, memory indirect, autoincrement, autodecrement, …)
More modes:
  + help better support programming constructs (array, pointer based accesses)
  -- make it harder for the architect to design
  -- many ways to do the same thing complicates compiler design

## Slide 15: Other Example ISA-level Tradeoffs
VLIW vs. single instruction
Precise vs. imprecise exceptions
Virtual memory vs. not
Unaligned access vs. not
Hardware interlocks vs. software-guaranteed interlocking
Software vs. hardware managed page fault handling
Cache coherence (hardware vs. software)
…

## Slide 16: RISC vs. CISC
RISC vs. CISC
  While type of ISA has a better performance?
  Is RISC more energy-efficient?
 | Format | Operations | Operands
RISC | Fixed length instructions Relatively simple encoding ARM/MIPS: 4B long | Simple, single function ops Single cycle | Operands: reg, imm Few addressing modes
CISC | Variable length instructions Common insts shorter/simpler Special insts longer/complex x86: from 1B to 16B long | Complex, multi-cycle insts | Operands: mem, reg, imm Many addressing modes

## Slide 17: RISC vs. CISC
Blem, Menon and Sankaralingam, “Power Struggles: Revisiting the RISC vs. CISC Debate on Contemporary ARM and x86 Architectures”, HPCA 2013.
  11 key findings
Conclusion: ISA being RISC or CISC does not matter for power and performance of modern processors

## Slide 18: Sample Question 1
C code:
int sum = 0; while (b != 0) {
sum += a;
b--;
} sum = sum + 100;
MIPS code?

## Slide 19: Sample Question 1
add $t0, $zero, $zero loop: beq $a1, $zero, finish add $t0, $t0, $a0 addi $a1, $a1, -1 j loop finish: addi $t0, $t0, 100

## Slide 20: Sample Question 2
Initially, $s3, $s4, $s5 contains i, j, k. Let $s6 stores the base of A[]. Each element of A is a 32-bit word.
MIPS instructions:
0 loop: add $t1, $s3, $s3 1 add $t1, $t1, $t1 2 add $t1, $t1, $s6 3 lw $t0, 0($t1) 4 bne $t0, $s5, exit 5 add $s3, $s3, $s4 6 j loop 7 exit:

## Slide 21: Sample Question 2
loop: add $t1, $s3, $s3 add $t1, $t1, $t1 add $t1, $t1, $s6 lw $t0, 0($t1) add $s3, $s3, $s4 bne $t0, $s5, exit j loop exit:
loop: t1 = 2i t1 = 4i t1 = s6 + 4i t0 = A[i] i = i + j if (A[i] != k) goto exit goto loop exit:
while (A[i] == k) { i = i + j; }

## Slide 22: Slide credits
Attiano Purpura-Pontoniere
Yuchen Hao
Onur Mutlu
James C. Hoe