## Slide 1: CS 33 – Discussion 1A Computer System Organization
Week 2

## Slide 2: Questions before we start?

## Slide 3: Logistics
Homework #1 due tonight
Lab 1 due next week Friday 4/17
TA site made for uploading disc recordings
  Also can upload anonymous feedback to improve disc

## Slide 4: Agenda
10am-11am PST:
x86-64 basics
Linux/Vim basics
Compilation/assembly code example
11am-11:50am PST:
LA worksheet

## Slide 5: x86-64 Basics – CISC/RISC
X86-64 is a CISC is a “Complex Instruction Set Computer”
  Started because instructions were more compact – instruction memory took up less space, a concern back when we had small memory capacity
  Many complex instructions possible
    Vector operations (SIMD)
    Single byte instructions (push/pop)
    many, many more
RISC is “Reduced Instruction Set Computer”
  Small set of fundamental instructions that get repeated
  Example architecture is MIPS
    (Microprocessor without Interlocked Pipelined Stages)
      I – R – J type instructions
        all instructions 32 bits

## Slide 6: x86-64 Basics - ISA
RISC and CISC are examples of an ISA
  Instruction System Architecture
    Essentially the interface between the hardware and software
    Defines the type of instructions we see in assembly
    Also defines the view of the hardware the complier sees (e.g. number of registers that can be used for register renaming/coloring)
Microarchitecture is the actual physical implementation of the ISA (digital circuits [NAND gates], sounds like fun right? If you want to keep going lower you reach analog circuits [BJT/CMOSFET transistors], even lower would be material science/semiconductor physics concerned with manufacturing the transistor diagrams [e.g. Molecular Beam Epitaxy or Photolithogrpahy or EBL])

## Slide 7: x86-64 Basics - Code
Machine code:
  The actual 10101..1110 binary encodings of instructions that correspond to high/low voltages for the circuit that defines your processor
Assembly code:
  Higher level than machine code but lower level than regular code
  Strong correspondence between instructions in assembly and object code (e.g. these 5 bytes are movl $0x01,%rax)

## Slide 8: x86-64 Basics - CPU

## Slide 9: x86-64 Basics – Memory layout
We assume memory is one large contiguous byte addressable array (we will see later this is an abstraction we can use thanks to virtual memory)

## Slide 10: x86-64 Basics – Memory layout
Stack contains the memory for the function call stack (grows downwards)
Heap contains the memory dynamically allocated (grows upwards
Memory in-between them is free until you over allocated (forgot to clean up memory that you “new”)
.bss is reserved space for uninitialized global/static vars
.data is reserved space for global/static variables
Text contains the instructions themselves

## Slide 11: x86-64 Basics – Memory layout
Early look at a stack frame
Func stack frame contains:
  Local vars
  Return addr
  Extra func args
    Cant fit in reg file
  Calle saved registers

## Slide 12: x86-64 Basics – text to object code

## Slide 13: Linux Basic Commands
pwd – print working directory
cd – change directory
ls – lists contents of directory (-a lists all, -l prints more info)
mkdir dir_name – makes a directory with dir_name
rm file/dir – removes file or dir (use –r flag for dir)
touch file_name.file_type – creates file_name.file_type in current dir
vim file_name.file_type – opens file_name.file_type (e.g. bits.c) with the vim text editor
emacs is an alternative text editor ( or nano)
  or you can develop locally and winscp files to seas

## Slide 14: Linux Basic Commands
gcc flags output_file input_files* - compiles input_files into output_file using a compiler that follows c coding standards
gdb – launches GNU debugger
  works for many languages like ada C/C++ fortran etc
  can set breakpoints and step through code
  print out stack traces
  disassemble object code (reverse engineer object code)
objdump –d obj_file – disassembles object file outside of gdb

## Slide 15: VIM Basic Commands
  gg – go to last line of doc
  G – go to first line of doc
  #G – go to line number #
  cntrl + f – move forward one screen
  cntrl + b – move back one screen
  i – switch to insert mode
  v – switch to visual mode (lets you select things to yank (copy) text
    y – yank (copy) marked text
    d – delete marked text
    > / < - shift left / right
  p – paste
  yy – copy line
  dd – cut line
  :w – write but don’t exit
  :wq – write and exit
  :q – quit, need to do :q! to force quit (drop any un-saved changes)
  /pattern – search for pattern, ?pattern searches backwards for pattern
  u - undo

## Slide 16: Compilation example

## Slide 17: Objectdump example

## Slide 18: Gdb example
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 19: x86-64 registers
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 20: x86-64 registers
%rip – instruction pointer, contains address for next ins for processor
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 21: x86-64 basic commands
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 22: x86-64 command suffixes
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 23: x86-64 operand types
Note you cannot use two memory operands in one operation
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents

## Slide 24: x86-64 addressing modes
Note you cannot use two memory accessing in one operation
Why?
Notes: Also show step = s, n = next, b <addr> is breakpoint there, l –lists code where the crash or bpoint, p var prints variable contents, I r – prints register contents, layout reg can show you what registers change in each ins

## Slide 25: Questions before we start worksheet?

## Slide 26: Resources used
https://cs.brown.edu/courses/cs033/docs/guides/x64_cheatsheet.pdf
https://cs.stackexchange.com/questions/76871/how-are-variables-stored-in-and-retrieved-from-the-program-stack
https://www.geeksforgeeks.org/memory-layout-of-c-program/
https://vim.rtorr.com/
https://www.tenouk.com/ModuleW.html
Professor Reinman’s slides (CCLE)
Credit for slides: Attiano Purpura-Potoniere