## Slide 1: CS 33 – Discussion 1A Computer System Organization
Week 6

## Slide 2: Questions before we start?

## Slide 3: Logistics
HW3 due tonight 11:59pm
Lab 2 – Attack lab released - Due Friday May 15th 11:59pm
Please submit suggestions on CCLE TA-site on how to improve OH or DISC
  Please fill out LA survey on CCLE if you haven’t already

## Slide 4: Agenda
10am-11am PST:
Memory Hierarchy
Attack lab spec
11am-11:50am PST:
LA worksheet

## Slide 5: Memory Basics
Memory technology
  SRAM – Registers/caches – 1-10 cycles access time
    L1/L2/L3 Cache data/instruction/unified
  DRAM – Volatile main memory
  Disk/Flash – Non-volatile main memory
  Communicate between types of memory with buses
    Bits driven out on parallel wires
Memory reference locality
  Spatial
  Temporal
Caching
  Subset of main memory with fast access
  Memory Mountain
  Matrix multiplication example

## Slide 6: Memory Basics

## Slide 7: Memory Basics
The memory hierarchy is composed of:
Caches
DRAM (4Gb, 2^32 bits)
  (can hypothetically fit entire address space in main memory if our word size is 32) (hundreds of cycles access time)
    Virtual memory gives each program illusion of having this
Disk (>1Tb, >2^40 bits) (millions of cycles access time)
Caches themselves have multiple levels:
  L1 (~Kb, ~2^10 bits) (~1-3 cycles access)
  L2/L3 (~Mb, ~2^20 bits)(~20-30 cycles access time L2)
    all levels have different sizes/policies/architectures

## Slide 8: Memory Basics

## Slide 9: Memory Basics

## Slide 10: Memory Basics

## Slide 11: Memory Basics

## Slide 12: Memory Basics

## Slide 13: Caching Basics
Physical memory isn’t the instantly accessible extremely large contiguous array we want it to be
Provide the fast access with the illusion of memory the size of disk by using caching and page tables for multiple programs
Want to exploit principles of temporal and spatial locality in good cache design to reduce the cost of accessing memory to the cost of just accessing the highest level cache

## Slide 14: Caching Basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
When data referenced
  HIT: if in cache, use cached data instead of accessing memory
  MISS: if not in cache, bring block into cache
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large, small, uniform blocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 15: Caching Basics

## Slide 16: Caching Basics

## Slide 17: Caching Basics

## Slide 18: Caching Basics

## Slide 19: Caching Basics

## Slide 20: Caching Basics

## Slide 21: Caching Basics

## Slide 22: Caching Basics

## Slide 23: Caching Basics

## Slide 24: Questions before we start worksheet?

## Slide 25: Resources used
Professor Reinman’s slides (CCLE)
Credit for compilation: Attiano Purpura-Pontoniere